## Slide 1
Information and Communication Theory
By
Dr. Hem Dutt Joshi
Associate Professor, ECED,
TIET, Patiala

## Slide 2: Lecture-1
Module-2 : Information Theory

## Slide 3: Course Content
Module-1 : Probability Theory
      Random Variable, Distribution function, Characteristic function and central limit theorem
Module-2 : Information Theory
      Information Measure, Entropy, Source coding, Mutual Information, channel capacity, Shannon’s Theorems.
Module-3 : Stochastic Processes
      Systems with Stochastic Inputs, Markov Chains, and Random-Walk Model
Module-4 : Estimation & Hypothesis Testing
      Hypothesis, Neyman Pearson Tests, Bayes’ Criteria, Z-Score, and p-Value Test
Module-5 : Statistical Modeling of Noise

## Slide 4: Content of Lecture-1
Communication System
Importance of Information Theory
Historical Origin of Information Theory
Information and Uncertainty
Information measure (Mathematical definition of Information)

## Slide 5: Communication System
Goal of Communication System is to transmit information from source to destination.
Information Source
  generates random messages for the transmission .
  Types of Messages are: Audio signal , Video signal, Image and Text
  Types of Information Source
    The Memory less Source:
      Generates Independent random messages .
    The Markov Source (Source with Memory):
      Generate dependent random messages
      Each symbol depends on previous symbol or state of source
Information
Source
Transmitter
Channel
Receiver
Destination
Message
Processed
Signal
Noisy
Signal
Estimate of Message
Notes: Some signal processing is done both at Transmitter and Receiver so that information can be transfer at maximum data rate without distortion .
We can control signal processing but not channel characteristics, so the questions are

## Slide 6: Communication System
Transmitter
  Process the message generated by information source so that it can be transmitted efficiently through the channel.
Receiver
  Receive the Noisy signal from channel.
  Apply signal processing to correctly estimate the transmitted message.
  It performs the inverse function of transmitter to reconstruct the original signal
Information
Source
Transmitter
Channel
Receiver
Destination
Message
Processed
Signal
Noisy
Signal
Estimate of Message
Notes: Some signal processing is done both at Transmitter and Receiver so that information can be transfer at maximum data rate without distortion .
We can control signal processing but not channel characteristics, so the questions are

## Slide 7: Communication System
Channel
  act as a medium of transmission.
  Channel may be wired or wireless.
Wired communication System
  Telephone communication system (channel: Two wire transmission line)
  Cable TV transmission system (Coaxial cable as a channel)
  Local area network (LAN) (Ethernet cables as a channel)
Wireless communication system
  Free space as a medium of transmission (channel)
  Cellular network (Mobile communication system)
  Satellite communication system
  FM, AM and TV broadcast system
Information
Source
Transmitter
Channel
Receiver
Destination
Message
Processed
Signal
Noisy
Signal
Estimate of Message
Notes: Some signal processing is done both at Transmitter and Receiver so that information can be transfer at maximum data rate without distortion .
We can control signal processing but not channel characteristics, so the questions are

## Slide 8: Communication System
Information
Source
Transmitter
Channel
Receiver
Destination
Message
Processed
Signal
Noisy
Signal
Estimate of Message
The major objective of any communication system is to transmit information with
  Maximum data rate
  Minimum probability of symbol error
  Minimum transmitted power
Now the questions are:
  how much maximum data rate can be supported by any communication system for reliable communication?
  What is the measure of information?
Notes: Some signal processing is done both at Transmitter and Receiver so that information can be transfer at maximum data rate without distortion .
We can control signal processing but not channel characteristics, so the questions are

## Slide 9: Information Theory
In particular, Information theory answers two fundamental questions:
  What is the irreducible complexity, below which a signal cannot be compressed?
    (Entropy of a source)
  What is the maximum transmission rate for reliable communication over a noisy channel?
    (Capacity of a channel)
In general, Information theory deals
  with the mathematical modeling and analysis of a communication system rather than with physical sources and physical channels.
  with the amount of information content in any random signal (Information Measure)
  Relationship between
    Signal to Noise Ratio and Channel Capacity
    Channel bandwidth and Capacity.

## Slide 10: Historical origins of Information Theory
The main concepts and principles of information theory were developed by Claude E. Shannon in late 1940s
  (C. E. Shannon, “ A Mathematical Theory of Communication “, Published in The Bell System Technical Journal, Vol. 27, pp. 379–423, 623–656, July, October, 1948)
  He did mathematical modeling and analysis of a communication system and postulates many theorems related to information theory.
The major contributions are -
  Source coding theorem,
  Channel coding theorem,
  Established relationship between signal to noise ratio and channel capacity, channel bandwidth and capacity.
Notes: prior to the publication of Shannon’s 1948 classic paper, it was
believed that increasing the rate of transmission over a channel would increase the
probability of error; the communication theory community was taken by surprise when
Shannon proved that this was not true, provided the transmission rate was below the
channel capacity.

## Slide 11: INFORMATION AND UNCERTAINTY
Consider following sentences:
The Sun rise in the east and set in the west
  ( Highly probable event , Probability is 1 )
Dog bites a man
  (It happen but not frequently-- associated with some probability or uncertainty )
There will be less rain in Patiala in this rainy season
  (It may also happen hence it is also associated with some probability)
Man bites a dog
  (Rarest event -- Highly uncertain)
The Thar desert will receive heavy rainfall in this rainy season
  (Rarest event -- Highly uncertain)

## Slide 12: INFORMATION AND UNCERTAINTY
Intuitive Feel:
  Information contained in an event is closely related to its uncertainty or probability
  Messages with low probability (i.e., highly unexpected messages) contains a large amount of information.
  Messages with high probability deliver very low amount of information.
  Before the event occurs,
    there is some amount of uncertainty.
  After the occurrence of the event,
    there is no uncertainty anymore, but there is gain in the amount of information.
    The amount of information should be inversely proportional to the probability of the message.

## Slide 13: Amount of Information (Mathematical Definition)
Let is an event with a probability , then the amount of information associated with is given as –
The choice of base for the logarithm define different units of information.
  When the base is ‘2’, then the unit of information is – bit
  When the base is ‘e’ then the unit of information is – nat
  When the base is ‘10’, then the unit of information is – decit or Hartley
, and
Self Information

## Slide 14: Amount of Information (Mathematical Definition)
This definition satisfied following properties
  Certain events convey no information
  Every event provides some information and never bring a loss of information
  Less probable event convey more information
Self Information

## Slide 15
The logarithmic measure is justified by the desire for information to be additive.
When two independent events take place then the total information is sum of information in each event. (Fourth Property)
But the probabilities of independent events multiply to give their combined probabilities,
Therefore, we must take Logarithms in order for the joint probability of independent events Or messages to contribute additively to the information gained.
Why Logarithm

## Slide 16: Why Logarithm
Let and are two independent event with a probability and respectively and self information associated with them is and
Let and ----- some function of probability
Then the probability of the joint event is define as –
Information associated with this joint event is define as
This total Information must be equal to the sum of individual information and
From above expression , it is clearly visible that we require a function which converts multiplication into addition and Logarithm is one such function.

## Slide 17: Reference Book
S. Haykin, Digital Communication Systems, John Wiley & Sons, NY, 2014.
R. Bose, Information theory, coding and cryptography, Publisher: Tata McGraw-Hill, 3rd Edition 2016.
R P Singh and S D Sapre, Communication System (Analog and Digital), Tata McGraw-Hill, 3rd Edition 2012.

## Slide 18: Thank you